## Slide 1
Chile Metropolitan Region Disasters
Enhancing Authority Response to Storm Floods in Chile Leveraging Automatic Satellite Image Processing
Virginia – Langley | Fall 2024
The Metropolitan Region in central Chile is home to approximately 7 million people. The region frequently experiences disastrous floods, impacting tens of thousands of people and millions of dollars in damages. Remote sensing methods used to map flooding extent can help emergency responders allocate resources efficiently. Partnering with Centro de Información de Recursos Naturales (CIREN) in collaboration with the Embassy of Chile Agricultural Office, we leveraged NASA Earth observations and hydraulic modeling to resolve flood extents for recent January 29, 2021, and August 23, 2023, flood events. Compared to the reported August 2023 flooding extents, the Earth observation and hydraulic modeling results were significantly less extensive. Additionally, we found that limited success of using optical and radar datasets to monitor riverine flood extents, while hydraulic modeling provides a more reliable tool for modeling future flood impacts within the Chile Metropolitan Region.
Project Synopsis
Estimate flood extent within the Metropolitan Region using a hydraulic model
Identify flooded areas in the Metropolitan Region using optical and radar datasets
Assess the feasibility of these methods to map flood extent in the Metropolitan Region
Objectives
Methodology
Study Area
We were able to resolve flood extents, evaluate flooding trends with elevation, and compare Earth observation methods for flood mapping
We found that hydraulic modeling is a feasible method for characterizing riverine floods, while optical imagery and SAR have limited success given issues with temporal and spatial constraints.
Conclusions
Acknowledgements
Centro de Información de Recursos Naturales (CIREN)
Embassy of Chile, Agricultural Office
Project Partners
Team Members
Isabella Giordano
Project Lead
Viviana Bravo Ortiz
Jackie Encinas
Patrick O'Shea
Data Acquisition
Data Processing
Data Analysis
Hydraulic Model
Optical
Radar
Sentinel-1 C-SAR GRD
Landsat 8 OLI
Landsat 9 OLI-2
Sentinel-2 MSI
HEC-RAS model
Stream flow data
SRTM 30-m DEM
Land cover
Geometry, flow & plan files
Diffusion Wave hydraulic model runs
Velocity, discharge, depth, flood extents
Terrain trends, floodplain widths
Mosaic & Clipping
Snow & cloud mask
Normalized Difference Water Index (NDWI)
NDWI change assessment
Radiometric Terrain Correction
Pixel spacing
Scale conversion
Log Difference to detect change in backscatter values
Earth Observations
Sentinel-2 MSI
Shuttle Radar Topography Mission
Landsat 9 OLI-2
Landsat 8 OLI
Sentinel-1 C-SAR
Km
N
Argentina
Bolivia
Peru
Chile
Santiago
Maipo River
Mapocho River
0 40 80 120 160
Km
N
Valparaíso
Libertador General Bernardo O'Higgins
Science Advisors
Dr. Xia Cai (Langley Research Center)
Dr. Kenton Ross (Langley Research Center)
Center Lead
Alyson Bergamini (VA – Langley)
Geoinformatics Fellow
Brooklyn Appling (VA – Langley)
Project partners and collaborators:​
CIREN
Carlos Calvo Cortés-Monroy
Vanessa Aros
Embassy of Chile
Fernando Vasquez
Andres Rodriguez
Adin Burwell
Metropolitan
Region Border
Rivers
Capital
0 1,800
ASF DAAC
Heidi Kristenson
James Milburn
ESRI
Vinay Viswambharan
Lisa Tanh
Results
Radar
January 26 & February 1, 2021
Optical
January 13 & February 2, 2021
Presence of rough features
Presence of standing water
Log Change Difference in Backscatter Value
7 Km
Figure 1b: Comparison of HEC-RAS (blue) and CIREN (green) flood extents for August 23, 2023
600
650
700
750
800
0
50
100
150
200
250
300
350
400
Floodplain Width (m)
August 23, 2023 Floodplain Width with Elevation: Model – CIREN Comparison
CIREN
Model
y = 0.27x + 29.76
y = -0.30x + 401.06
Elevation (m)
R2 = 0.08
R2 = 0.08
Figure 1a: Evaluation of floodplain width and elevation during the August 23, 2023 flood event
Figure 2a: Change in water as calculated from optical data from the January 29, 2021 flood event
Figure 2b: Change in water as calculated from radar data from January 29, 2021 flood event
Increase in water
Decrease in Water
Change in NDWI
7 Km